RTCD136  SERIES　　　（ 105℃ 2000H）

●Compliant to the RoHS directive.

●25WV~450WV Standard products 2000H at 105℃.

■Product Specifications

| (unit: mm) | Items | Specifications |
| --- | --- | --- |
|  | Temperature range | -40℃~+105℃ | -25℃~+105℃ |
|  | Rated voltage | 25~160V.DC | 200~550V.DC |
|  | Capacitance tolerance | ±20% (20℃, 120Hz) |
|  | Leakage current | 0.01CV (μA) or 5 mA,whichever is smaller or less |
|  |  | [ C=nominal capacitance (μF),V= rated voltage (V) ] |
|  | Dissipation factor | Less than the value specified in the standard products table. |
|  | Permissible ripple current | As specified in the standard products table. (105℃, 120Hz) |
| ΦD | P | S | T | Cap material |  | High-temperature load | After the rated voltage with specified ripple current is applied at 105℃ for 2000 hours : Capacitance tolerance : ±20% or less of the initial value Dissipation factor : 200% or less of the specified initial value Leakage current : Specified initial value or less |
| 36 | 12.7 | M5×10 | 6.0 | Phenol |  |  |  |
| 51 | 22.0 | M5×10 | 5.5 | Phenol |  |  |  |
| 64 | 28.6 | M5×10 | 5.5 | Phenol |  |  |  |
| 77 | 32.0 | M5×10 | 4.5 | Phenol |  |  |  |
| 90 | 32.0 | M5×10 | 4.0 | Phenol |  | 执行标准 | JIS C 5101-4 |

| Ripple current correction coefficient |  | Part number(Example):RTCD136 400V 10,000μF±20% F case（Φ90mm）product |
| --- | --- | --- |
| Temperature (℃) | 40 | 55 | 70 | 85 | 105 |  | RTCD136 2G 103 Y F 196 M D 5 Series Voltage Code Capacitance code Mounting style Diameter code Length Cap. tolerance Diameter Terminal Type of screw |
| Coefficient | 250WV under | 4.9 | 3.9 | 3.0 | 1.8 | 1.0 |  |  |
|  | 400WV | 3.8 | 3.3 | 2.5 | 2.0 | 1.0 |  |  |
| Frequency (Hz) | 50/60 | 120 | 300 | 1K | ≥10K |  |  |
| Coefficient | 0.8 | 1.0 | 1.1 | 1.3 | 1.4 |  |  |

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 25 1E (32) | 10000 | 36×53 | 0.35 | 2.9 | 32 | 30 | RTCD1361E103IA053M |
|  | 15000 | 36×83 | 0.35 | 4.2 | 27 | 27 | RTCD1361E153IA083M |
|  | 22000 | 36×83 | 0.35 | 5.1 | 22 | 23 | RTCD1361E223IA083M |
|  | 33000 | 36×100 | 0.40 | 6.3 | 15 | 16 | RTCD1361E333IA100M |
|  | 47000 | 51×75 | 0.40 | 8.0 | 10 | 11 | RTCD1361E473YC075M |
|  | 68000 | 51×115 | 0.50 | 10.0 | 7 | 8 | RTCD1361E683YC115M |
|  | 100000 | 64×96 | 0.60 | 11.3 | 6 | 7 | RTCD1361E104YD096M |
|  | 150000 | 64×115 | 0.80 | 12.9 | 6 | 7 | RTCD1361E154YD115M |
|  | 220000 | 77×115 | 1.00 | 14.8 | 4 | 5 | RTCD1361E224YE115M |
|  | 330000 | 90×131 | 1.00 | 19.9 | 4 | 5 | RTCD1361E334YF131M |
| 35 1V (44) | 6800 | 36×53 | 0.30 | 2.6 | 42 | 37 | RTCD1361V682IA053M |
|  | 10000 | 36×83 | 0.30 | 3.7 | 29 | 31 | RTCD1361V103IA083M |
|  | 15000 | 36×83 | 0.30 | 4.5 | 19 | 20 | RTCD1361V153IA083M |
|  | 22000 | 36×100 | 0.35 | 5.5 | 14 | 15 | RTCD1361V223IA100M |
|  | 33000 | 51×75 | 0.40 | 6.7 | 12 | 13 | RTCD1361V333YC075M |
|  | 47000 | 51×96 | 0.45 | 8.1 | 8 | 9 | RTCD1361V473YC096M |
|  | 68000 | 51×115 | 0.50 | 10.0 | 7 | 8 | RTCD136A1V683YC115M |
|  | 100000 | 64×115 | 0.60 | 12.1 | 6 | 7 | RTCD1361V104YD115M |
|  | 150000 | 77×115 | 0.70 | 13.8 | 5 | 7 | RTCD1361V154YE115M |
|  | 220000 | 90×131 | 0.70 | 17.6 | 5 | 7 | RTCD1361V224YF131M |

■Standard Products Table

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 50 1H (63) | 3300 | 36×53 | 0.20 | 2.2 | 90 | 80 | RTCD1361H332IA053M |
|  | 4700 | 36×53 | 0.25 | 3.3 | 64 | 58 | RTCD1361H472IA053M |
|  | 6800 | 36×83 | 0.25 | 3.4 | 44 | 39 | RTCD1361H682IA083M |
|  | 10000 | 36×83 | 0.25 | 4.1 | 30 | 28 | RTCD1361H103IA083M |
|  | 15000 | 36×100 | 0.30 | 4.9 | 20 | 20 | RTCD1361H153IA100M |
|  | 22000 | 51×75 | 0.35 | 5.9 | 14 | 15 | RTCD1361H223YC075M |
|  | 33000 | 51×115 | 0.40 | 7.8 | 13 | 14 | RTCD1361H333YC115M |
|  | 47000 | 64×96 | 0.40 | 9.5 | 11 | 12 | RTCD1361H473YD096M |
|  | 68000 | 64×115 | 0.45 | 11.6 | 8 | 9 | RTCD1361H683YD115M |
|  | 100000 | 77×115 | 0.50 | 14.1 | 6 | 7 | RTCD1361H104YE115M |
|  | 150000 | 90×131 | 0.50 | 18.9 | 5 | 7 | RTCD1361H154YF131M |
| 63 1J (79) | 2200 | 36×53 | 0.15 | 2.1 | 95 | 87 | RTCD1361J222IA053M |
|  | 3300 | 36×53 | 0.20 | 2.2 | 63 | 58 | RTCD1361J332IA053M |
|  | 4700 | 36×83 | 0.20 | 3.1 | 54 | 50 | RTCD1361J472IA083M |
|  | 6800 | 36×83 | 0.20 | 3.7 | 38 | 35 | RTCD1361J682IA083M |
|  | 10000 | 36×100 | 0.25 | 4.4 | 28 | 28 | RTCD1361J103IA100M |
|  | 15000 | 51×75 | 0.25 | 5.7 | 21 | 22 | RTCD1361J153YC075M |
|  | 22000 | 51×96 | 0.30 | 6.8 | 13 | 14 | RTCD1361J223YC096M |
|  | 33000 | 64×96 | 0.30 | 9.2 | 10 | 11 | RTCD1361J333YD096M |
|  | 47000 | 64×115 | 0.35 | 10.9 | 8 | 9 | RTCD1361J473YD115M |
|  | 68000 | 77×115 | 0.40 | 13.0 | 7 | 8 | RTCD1361J683YE115M |
|  | 100000 | 90×131 | 0.40 | 17.2 | 7 | 8 | RTCD1361J104YF131M |
| 80 1K (100) | 2200 | 36×53 | 0.15 | 2.1 | 68 | 63 | RTCD1361K222IA053M |
|  | 3300 | 36×83 | 0.15 | 3.0 | 45 | 42 | RTCD1361K332IA083M |
|  | 4700 | 36×83 | 0.15 | 3.6 | 32 | 30 | RTCD1361K472IA083M |
|  | 6800 | 36×100 | 0.20 | 4.0 | 22 | 23 | RTCD1361K682IA100M |
|  | 10000 | 51×75 | 0.20 | 5.2 | 15 | 16 | RTCD1361K103YC075M |
|  | 15000 | 51×96 | 0.25 | 6.2 | 10 | 11 | RTCD1361K153YC096M |
|  | 22000 | 64×96 | 0.25 | 8.2 | 9 | 10 | RTCD1361K223YD096M |
|  | 33000 | 77×96 | 0.30 | 9.7 | 7 | 7 | RTCD1361K333YE096M |
|  | 47000 | 77×115 | 0.30 | 12.5 | 6 | 7 | RTCD1361K473YE115M |
|  | 68000 | 90×131 | 0.30 | 16.4 | 4 | 7 | RTCD1361K683YF131M |
| 100 2A (125) | 1000 | 36×53 | 0.15 | 1.4 | 112 | 100 | RTCD1362A102IA053M |
|  | 1500 | 36×53 | 0.15 | 1.7 | 75 | 67 | RTCD1362A152IA053M |
|  | 2200 | 36×83 | 0.15 | 2.5 | 51 | 47 | RTCD1362A222IA083M |
|  | 3300 | 36×83 | 0.15 | 3.0 | 34 | 32 | RTCD1362A332IA083M |
|  | 4700 | 36×100 | 0.15 | 3.9 | 24 | 24 | RTCD1362A472IA100M |
|  | 6800 | 51×75 | 0.15 | 5.0 | 19 | 20 | RTCD1362A682YC075M |
|  | 10000 | 51×96 | 0.15 | 6.5 | 13 | 14 | RTCD1362A103YC096M |
|  | 15000 | 64×96 | 0.20 | 7.6 | 11 | 12 | RTCD1362A153YD096M |
|  | 22000 | 77×96 | 0.20 | 9.7 | 8 | 9 | RTCD1362A223YE096M |
|  | 33000 | 77×130 | 0.25 | 11.8 | 6 | 7 | RTCD1362A333YE130M |
|  | 47000 | 90×131 | 0.25 | 15.0 | 5 | 7 | RTCD1362A473YF131M |
| 160 2C (200) | 470 | 36×53 | 0.15 | 1.0 | 277 | 261 | RTCD1362C471IA053M |
|  | 680 | 36×53 | 0.15 | 1.1 | 191 | 180 | RTCD1362C681IA053M |
|  | 1000 | 36×83 | 0.15 | 1.7 | 130 | 120 | RTCD1362C102IA083M |
|  | 1500 | 36×83 | 0.15 | 2.0 | 87 | 80 | RTCD1362C152IA083M |
|  | 2200 | 36×100 | 0.15 | 2.7 | 59 | 53 | RTCD1362C222IA100M |
|  | 3300 | 51×75 | 0.15 | 3.5 | 40 | 35 | RTCD1362C332YC075M |
|  | 4700 | 51×96 | 0.15 | 4.4 | 30 | 25 | RTCD1362C472YC096M |
|  | 6800 | 64×96 | 0.15 | 5.9 | 22 | 23 | RTCD1362C682YD096M |
|  | 10000 | 77×96 | 0.15 | 7.6 | 15 | 16 | RTCD1362C103YE096M |
|  | 15000 | 77×130 | 0.15 | 10.3 | 14 | 14 | RTCD1362C153YE130M |
|  | 22000 | 90×131 | 0.15 | 13.2 | 10 | 10 | RTCD1362C223YF131M |
| 200 2D (250) | 330 | 36×53 | 0.15 | 0.8 | 381 | 372 | RTCD1362D331IA053M |
|  | 470 | 36×53 | 0.15 | 1.0 | 270 | 261 | RTCD1362D471IA053M |
|  | 680 | 36×53 | 0.15 | 1.1 | 187 | 180 | RTCD1362D681IA053M |
|  | 1000 | 36×83 | 0.15 | 1.7 | 120 | 100 | RTCD1362D102IA083M |
|  | 1500 | 36×100 | 0.15 | 2.2 | 81 | 85 | RTCD1362D152IA100M |
|  | 2200 | 51×75 | 0.15 | 2.8 | 68 | 60 | RTCD1362D222YC075M |
|  | 3300 | 51×96 | 0.15 | 3.7 | 45 | 35 | RTCD1362D332YC096M |
|  | 4700 | 64×96 | 0.15 | 4.9 | 31 | 27 | RTCD1362D472YD096M |
|  | 6800 | 64×115 | 0.15 | 0.3 | 21 | 20 | RTCD1362D682YD115M |
|  | 10000 | 77×115 | 0.15 | 8.1 | 14 | 14 | RTCD1362D103YE115M |
|  | 15000 | 90×130 | 0.15 | 10.9 | 10 | 10 | RTCD1362D153YF130M |

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 250 2E (300) | 330 | 36×53 | 0.15 | 0.8 | 165 | 268 | RTCD1362E331IA053M |
|  | 470 | 36×53 | 0.15 | 1.0 | 126 | 187 | RTCD1362E471IA053M |
|  | 680 | 36×83 | 0.15 | 1.4 | 91 | 131 | RTCD1362E681IA083M |
|  | 1000 | 36×100 | 0.15 | 1.9 | 59 | 70 | RTCD1362E102IA100M |
|  | 1500 | 51×75 | 0.15 | 2.3 | 45 | 50 | RTCD1362E152YC075M |
|  | 2200 | 51×96 | 0.15 | 3.1 | 33 | 45 | RTCD1362E222YC096M |
|  | 3300 | 64×96 | 0.15 | 4.2 | 25 | 35 | RTCD1362E332YD096M |
|  | 4700 | 64×115 | 0.15 | 5.4 | 19 | 23 | RTCD1362E472YD115M |
|  | 6800 | 77×115 | 0.15 | 6.9 | 13 | 18 | RTCD1362E682YE115M |
|  | 10000 | 77×155 | 0.15 | 9.3 | 11 | 13 | RTCD1362E103YE155M |
|  | 15000 | 90×157 | 0.15 | 12.2 | 9 | 9 | RTCD1362E153YF157M |
| 400 2G (450) | 1000 | 51×75 | 0.15 | 2.5 | 86 | 105 | RTCD1362G102YC075M |
|  | 1200 | 51×96 | 0.15 | 3.0 | 77 | 88 | RTCD1362G122YC096M |
|  | 1500 | 51×115 | 0.15 | 3.6 | 53 | 70 | RTCD1362G152YC115M |
|  | 1800 | 51×130 | 0.15 | 4.1 | 43 | 58 | RTCD1362G182YC130M |
|  | 2200 | 64×96 | 0.15 | 4.5 | 36 | 48 | RTCD1362G222YD096M |
|  | 2700 | 64×115 | 0.15 | 5.3 | 27 | 40 | RTCD1362G272YD115M |
|  | 3300 | 64*115 | 0.15 | 5.8 | 24 | 32 | RTCD1362G332YD115M |
|  |  | 64×130 | 0.15 | 6.2 | 24 | 32 | RTCD1362G332YD130M |
|  | 3900 | 64×155 | 0.15 | 7.2 | 22 | 28 | RTCD1362G392YD155M |
|  |  | 77×115 | 0.15 | 6.8 | 22 | 28 | RTCD1362G392YE115M |
|  | 4700 | 64×195 | 0.15 | 8.7 | 17 | 22 | RTCD1362G472YD195M |
|  |  | 77*115 | 0.15 | 7.3 | 17 | 22 | RTCD1362G472YE115M |
|  |  | 77×130 | 0.15 | 7.8 | 17 | 22 | RTCD1362G472YE130M |
|  | 5600 | 64×195 | 0.15 | 9.6 | 15 | 19 | RTCD1362G562YD195M |
|  |  | 77*130 | 0.15 | 9.2 | 15 | 19 | RTCD1362G562YE130M |
|  |  | 77×155 | 0.15 | 9.2 | 15 | 19 | RTCD1362G562YE155M |
|  | 6800 | 77*145 | 0.15 | 9.5 | 14 | 15 | RTCD1362G682YE145M |
|  |  | 77*155 | 0.15 | 9.5 | 14 | 15 | RTCD1362G682YE155M |
|  |  | 90×157 | 0.15 | 10.7 | 14 | 15 | RTCD1362G682YF157M |
|  | 8200 | 90*130 | 0.15 | 10.5 | 12 | 15 | RTCD1362G822YF130M |
|  |  | 90×157 | 0.15 | 11.8 | 12 | 15 | RTCD1362G822YF157M |
|  | 10000 | 77*195 | 0.15 | 12 | 10 | 15 | RTCD1362G103YE195M |
|  |  | 90*130 | 0.15 | 11.9 | 10 | 15 | RTCD1362G103YF130M |
|  |  | 90×196 | 0.15 | 14.1 | 10 | 15 | RTCD1362G103YF196M |
| 450 2W (500) | 220 | 36×53 | 0.15 | 1.2 | 415 | 427 | RTCD1362W221YA053M |
|  | 330 | 36×100 | 0.15 | 1.5 | 277 | 286 | RTCD1362W331YA100M |
|  | 470 | 51×83 | 0.15 | 2.2 | 195 | 201 | RTCD1362W471YC083M |
|  | 680 | 51×96 | 0.15 | 2.8 | 135 | 139 | RTCD1362W681YC096M |
|  | 1000 | 51×100 | 0.15 | 4.2 | 90 | 93 | RTCD1362W102YC100M |
|  | 1500 | 51×130 | 0.15 | 5.8 | 54 | 56 | RTCD1362W152YC130M |
|  | 2200 | 64×115 | 0.15 | 7.4 | 33 | 34 | RTCD1362W222YD115M |
|  | 3300 | 77×130 | 0.15 | 10.1 | 22 | 23 | RTCD1362W332YE130M |
|  | 3900 | 64*140 | 0.15 | 102. | 22 | 23 | RTCD1362W392YD140M |
|  |  | 64*155 | 0.15 | 10.5 | 22 | 23 | RTCD1362W392YD155M |
|  |  | 77*130 | 0.15 | 10.9 | 22 | 23 | RTCD1362W392YE130M |
|  | 4000 | 77*220 | 0.15 | 11.5 | 22 | 23 | RTCD1362W402YE220M |
|  | 4700 | 77*155 | 0.15 | 12.7 | 15 | 15 | RTCD1362W472YE155M |
|  | 5600 | 77*155 | 0.15 | 14.3 | 11 | 11 | RTCD1362W562YE155M |
|  |  | 90*157 | 0.15 | 15.8 | 11 | 11 | RTCD1362W562YF157M |
|  | 6800 | 77*170 | 0.15 | 17.2 | 11 | 11 | RTCD1362W682YE170M |
|  |  | 90*130 | 0.15 | 18.8 | 11 | 11 | RTCD1362W682YF130M |
|  |  | 90*157 | 0.15 | 19.4 | 11 | 11 | RTCD1362W682YF157M |
|  | 8200 | 77*170 | 0.15 | 20.0 | 11 | 11 | RTCD1362W822YE170M |
|  | 10000 | 90*157 | 0.15 | 22.0 | 11 | 11 | RTCD1362W103YF157M |
|  | 12000 | 90*220 | 0.15 | 28.2 | 11 | 11 | RTCD1362W123YF220M |

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 500 2H (550) | 470 | 51*80 | 0.15 | 3.0 | 200 | 220 | RTCD1362H471YC080M |
|  | 680 | 51*100 | 0.15 | 3.8 | 180 | 200 | RTCD1362H681YC100M |
|  | 1000 | 51*120 | 0.15 | 5.1 | 160 | 180 | RTCD1362H102YC120M |
|  | 1500 | 64*115 | 0.15 | 6.9 | 140 | 160 | RTCD1362H152YD115M |
|  | 2200 | 64*130 | 0.15 | 7.3 | 120 | 140 | RTCD1362H222YD130M |
|  |  | 77*115 | 0.15 | 8.1 | 120 | 140 | RTCD1362H222YE115M |
|  |  | 77*130 | 0.15 | 8.1 | 120 | 140 | RTCD1362H222YE130M |
|  | 2700 | 64*155 | 0.15 | 10.6 | 100 | 120 | RTCD1362H272YD155M |
|  | 3300 | 77*150 | 0.15 | 11.8 | 80 | 100 | RTCD1362H332YE150M |
|  |  | 77*155 | 0.15 | 11.8 | 80 | 100 | RTCD1362H332YE155M |
|  | 3900 | 77*155 | 0.15 | 13.0 | 60 | 80 | RTCD1362H332YE155M |
|  | 4700 | 90*150 | 0.15 | 15.0 | 40 | 60 | RTCD1362H472YF150M |
|  | 5600 | 90*157 | 0.15 | 16.3 | 35 | 40 | RTCD1362H562YF157M |
|  | 6800 | 90*170 | 0.15 | 17.9 | 30 | 35 | RTCD1362H682YF170M |
|  |  | 90*196 | 0.15 | 17.9 | 30 | 35 | RTCD1362H682YF196M |
|  | 8200 | 90*220 | 0.15 | 23.4 | 20 | 30 | RTCD1362H822YF220M |
|  | 10000 | 90*263 | 0.15 | 26.8 | 15 | 25 | RTCD1362H103YF263M |
| 550 2Y (600) | 470 | 51*100 | 0.15 | 3.2 | 190 | 195 | RTCD1362Y471YC100M |
|  | 680 | 51*120 | 0.15 | 4.2 | 170 | 180 | RTCD1362Y681YC120M |
|  | 1000 | 64*115 | 0.15 | 5.6 | 150 | 170 | RTCD1362Y102YD115M |
|  | 1500 | 64*130 | 0.15 | 7.5 | 130 | 150 | RTCD1362Y152YD130M |
|  | 2200 | 64*155 | 0.15 | 8.9 | 110 | 120 | RTCD1362Y222YD155M |
|  | 2700 | 77*150 | 0.15 | 11.5 | 90 | 100 | RTCD1362Y272YE150M |
|  | 3300 | 77*155 | 0.15 | 13.0 | 70 | 80 | RTCD1362Y332YE155M |
|  | 3900 | 90*150 | 0.15 | 14.3 | 50 | 60 | RTCD1362Y392YF150M |
|  | 4700 | 90*157 | 0.15 | 16.2 | 40 | 50 | RTCF1362Y472YF157M |
|  | 5600 | 90*196 | 0.15 | 20.6 | 30 | 35 | RTCD1362Y562YF196M |
|  | 6800 | 90*220 | 0.15 | 25.0 | 25 | 30 | RTCD1362Y682YF220M |
|  | 8200 | 90*263 | 0.15 | 28.5 | 20 | 25 | RTCD1362Y822YF263M |